## Slide 1: Introduction to Microsoft Robotics Studio with Lego NXT
Brian Peek

## Slide 2: Agenda
Overview of MSRS and its architecture
Using MSRS via code
Using MSRS via Visual Programming Language
Building a functional robot
Simulation Engine

## Slide 3: What is it?
Windows-based runtime built on .NET which consists of three “applications”
  Code-based runtime which drive physical machine
  Visual Programming Language which allows software building via “drag-and-drop” components
  Simulation engine to test robots which one does not physically have access to
Service-based architecture which handles the complexities of concurrency, coordination and decentralization

## Slide 4: CCR and DSS
CCR – Concurrency and Coordination Runtime
  Provides near-automatic coordination of messages without burdening the developer with the hassles of threading, semaphores, etc.
DSS – Decentralized System Services
  Hosts services locally or remotely and provides basic services for debugging, logging, monitoring, etc.

## Slide 5: Services
Basic building block of all applications
Contains implementation of a specific sensor, motor, platform, or coordination of a group of other services
Services are “partnered” with each other
Generic services exist to provide hardware abstraction
Service host started at command prompt, environment exposed via HTTP

## Slide 6: Creating a Service
From Microsoft Robotics Studio Command Prompt:
  dssnewservice /service:LegoEx1
  Creates directory, solution and base source code required for a full MSRS service
  Add /language:vb for a Visual Basic service

## Slide 7: Service Files
LegoEx1.cs – Service implementation
LegoEx1Types.cs – Message types and state object
LegoEx1.manifest.xml – Configuration information and services partnered at runtime

## Slide 8: Manifest Files
Manifest files are XML files which describe what services are run at startup
Contain configuration information about specific hardware types
When using generic services (motor, bumper, etc.) one can change hardware platforms simply by changing manifest files
Lego NXT services come with several pre-written manifest files to get you up and going quickly!

## Slide 9: Setup and Configure NXT Brick
Bluetooth is a pain
Ensure Bluetooth is enabled on brick
Initiate connection from PC
Enter passkey as 1234
Note COM Port installed on
Run:
  dsshost -port:50000 -tcpport:50001 -manifest:”samples\Config\LEGO.NXT.Brick.manifest.xml“
Browse to:
  http://localhost:50000/legonxt/0bcbf164-c568-43c5-a9e3-61d47a541a24
Enter COM port from above
Submit
Ensure software is downloaded and started on brick
When page refreshes, you may configure how sensors and motors operate

## Slide 10: Let’s Start Building!
Service via code - LegoEx1

## Slide 11: What We Did
Created a new service
Looked at parts making up a service
  State
  Message types
  Partnering with services
Added a contact sensor
Added a motor
Added a differential drive service

## Slide 12: Visual Programming Language
Same examples with VPL

## Slide 13: What We Did
Overview of VPL environment
Re-created previous example using VPL
Pros
  Very easy to use
  Fully functional programming language
Cons
  Cannot create new hardware platform using VPL
  Can get very complex very quickly

## Slide 14: Tie It Together
Building a functional robot via code and VPL

## Slide 15: Simulation Enviroment
Can be started via code or icon
Provides a way to use MSRS without the actual robotics hardware
Physics and graphics engine allow for an experience that emulates the real world
For building custom robots, can be very complex as artwork and modeling is required for accurate representation

## Slide 16: Simulation Environment
A brief overview of what the simulation environment is and how it works

## Slide 17: Conclusion
MSRS is a very complex and feature rich environment for developing robotics software
Existing platforms allow one to easily get up and running
Generic/abstract services allow platform independence
CCR/DSS implement a lot of the grunt work required for concurrent and distributed programming
VPL provides for an easy-to-use rapid prototyping environment or simple robot design
Lego NXT is a very capable platform for building simple to moderately complex robots

## Slide 18: More Information
http://msdn.microsoft.com/robotics/
http://msdn.microsoft.com/coding4fun/robotics/
http://www.brianpeek.com/
brian@brianpeek.com

## Slide 19: Questions?