## Slide 1: Interfacing External Hardware Using Managed Code and Microsoft Robotics Studio
Brian Peek

## Slide 2: Agenda
Easy: Phidgets
  RFID reader and tags
  Phidget Interface Kits
  I/O, both digital and analog
Intermediate: Servo controller
  Serial-based device
Difficult: Microsoft Robotics Studio
  Using some of the above in the MSRS environment

## Slide 3: RFID
Radio-frequence Identification
Various standards which vary based on frequency and data length
Passive vs. Active
  Passive can be read from ½ - ~4” away without special hardware (even then, only 6-12”)
  Active can be read up to 300 feet but require power source
Works via induction
  RF signal sent by reader induces electrical current in antenna located in RFID device
  Small current is enough power to transmit a response from the embedded CMOS IC

## Slide 4: RFID & Phidgets
Phidget board specifics:
  EM4102 standard
    125KHz
    Read-only
  40-bit unique identifier returned as hex string
    1,099,511,627,776 unique values
  4 outputs:
    5V for toggling relay on/off
    External LED
    Internal LED
    Antenna on/off
All controlled via eventing interface in .NET

## Slide 5: Phidget RFID Example
C# code to read value from RFID tag

## Slide 6: Phidget Interface Kit 0/4/4
  Output board with 4 mechanical relays
    Used to switch high-current devices
    I used this for my Christmas Lights project to switch strings of lights to music

## Slide 7: Phidget Interface Kit 0/16/16
  0/16/16 – 16 digital outputs, 16 digital inputs
    Used for digital I/O only (switches, LEDs, driving external devices)
    Inputs of 4 to 30V read as high
    Inputs of 0-3V read as low
    Provide external power for outputs, can sink up to 30V DC at 2 A.
    I used this with my R/C car project to toggle the switches used in the handset

## Slide 8: Phidget Interface Kit 8/8/8
  8/8/8 – 8 analog inputs, 8 digital inputs, 8 digital outputs
    Same as 0/16/16 with the addition of reading analog sensors (temperature, sonar, accelermeter)
    Digital Inputs are switch triggered, should not apply voltage
    Digital outputs are +5V when on and 0V when off
    Analog inputs receive voltage between 0 and +5V
      Converted into a value between 0 and 1000
    Provides a USB hub for easy linking

## Slide 9: Phidget Interafce Kit Examples
Overview of Christmas Lights
Simple example of analog inputs

## Slide 10: Servos
Positional vs. Continuous Rotation
Pulse Width Modulation (PWM)
  Pulses are sent every 20ms which last from 1 to 2 ms in length (width)
  1.5ms length pulses equate to centered/stopped
  1ms is 180° in one direction/full speed in one direction
  2ms is 180° in the other/full speed in the other

## Slide 11: Lynxmotion SSC-32 Servo Controller
32 channels of 1uS resolution
Bidirectional communication (read and write)
Controlled via serial port and standard text commands
  #<ch> P<pulse width> S<speed> … #<ch> etc. <cr>
  Ex: #5 P1600 S750 <cr>
    Move servo 5 to position 1600 at 750uS per second until it reaches destination
Plenty of additional commands to handle offsets for calibration, querying of servo states, hexapod sequences, etc.

## Slide 12: Lynxmotion SSC-32 Servo Controller Example
Code to drive servos using SSC-32 via .NET SerialPort class

## Slide 13: Microsoft Robotics Studio
Windows-based runtime built on .NET which consists of three “applications”
  Code-based runtime which drive physical machine
  Visual Programming Language which allows software building via “drag-and-drop” components
  Simulation engine to test robots which one does not physically have access to
Service-based architecture which handles the complexities of concurrency, coordination and decentralization

## Slide 14: CCR and DSS
CCR – Concurrency and Coordination Runtime
  Provides near-automatic coordination of messages without burdening the developer with the hassles of threading, semaphores, etc.
DSS – Decentralized System Services
  Hosts services locally or remotely and provides basic services for debugging, logging, monitoring, etc.

## Slide 15: Services
Basic building block of all applications
Contains implementation of a specific sensor, motor, platform, or coordination of a group of other services
Services are “partnered” with each other
Generic services exist to provide hardware abstraction
Service host started at command prompt, environment exposed via HTTP

## Slide 16: Creating a Service
From Microsoft Robotics Studio Command Prompt:
  dssnewservice /service:MSRSEx1
  Creates directory, solution and base source code required for a full MSRS service
  Add /language:vb for a Visual Basic service

## Slide 17: Service Files
MSRSEx1.cs – Service implementation
MSRSEx1Types.cs – Message types and state object
MSRSEx1.manifest.xml – Configuration information and services partnered at runtime

## Slide 18: Microsoft Robotics Studio Example
Service via code which will communicate Phidget Interface Kit to control R/C car

## Slide 19: Visual Programming Language
Drag and drop environment build on Windows Workflow Foundation (WF)
Can create new service using existing services, but cannot create service from scratch
Easy to use and quite powerful
Great for rapid prototyping of a service where full control is not needed

## Slide 20: Visual Programming Language
Same example with VPL

## Slide 21: More Information
Phidgets
  http://www.phidgets.com/
  http://www.trossenrobotics.com/
Lynxmotion SSC-32 Servo Controller
  http://www.lynxmotion.com/
Microsoft Robotics Studio
  http://msdn.microsoft.com/robotics/
  http://msdn.microsoft.com/coding4fun/robotics/
Me
  http://www.brianpeek.com/
  brian@brianpeek.com

## Slide 22: Questions?