## Slide 1: Introduction to Microsoft Robotics Studio with Lego NXT
Brian Peek
http://www.brianpeek.com/
brian@brianpeek.com

## Slide 2: Agenda
Overview of MSRS and its architecture
Using MSRS via Visual Programming Language
Using MSRS via code
Building a functional robot
Simulation Engine

## Slide 3: What is Lego NXT?
Latest Mindstorms kit by Lego (late 2006)
Contents:
  Brick – CPU and I/O ports
    Bluetooth + USB connectivity
  Touch sensor
  Sound sensor
  Light sensor
  Ultrasonic sensor
  Servos
  Many, many parts, but not like typical Legos
  Software
Priced at ~$250

## Slide 4: What is MSRS?
Windows-based runtime built on .NET which consists of three “applications”
  Code-based runtime which drive physical machine
  Visual Programming Language which allows software building via “drag-and-drop” components
  Simulation engine to test robots which one does not physically have access to
Service-based architecture which handles the complexities of concurrency, coordination and decentralization

## Slide 5: CCR and DSS
CCR – Concurrency and Coordination Runtime
  Provides near-automatic coordination of messages without burdening the developer with the hassles of threading, semaphores, etc.
DSS – Decentralized System Services
  Hosts services locally or remotely and provides basic services for debugging, logging, monitoring, etc.

## Slide 6: Services
Basic building block of all applications
Contains implementation of a specific sensor, motor, platform, or coordination of a group of other services
Services are “partnered” with each other
Generic services exist to provide hardware abstraction
Support for several platforms exists right out of the box, including LegoNXT
Service information exposed via
An application itself is a service

## Slide 7: Setup and Configure NXT Brick
Bluetooth is a pain
Ensure Bluetooth is enabled on brick
Always initiate connection from PC
Enter passkey as 1234
Note COM Port installed on (outgoing port)

## Slide 8: Visual Programming Language (VPL)
Exactly as it says, it’s a visual programming language
Targeted at beginners, but is very powerful for rapid prototyping
C# code can be generated from VPL diagram and edited directly
BUT it’s a one-way process…C# cannot be converted back to VPL

## Slide 9: Visual Programming Language
Some examples with VPL

## Slide 10: What We Did
Overview of VPL environment
Pros
  Very easy to use
  Fully functional programming language
Cons
  Cannot create new hardware platform using VPL
  Can get very complex very quickly

## Slide 11: MSRS via C#
Code is extremely complex due to CCR
Unless you’re building a new platform or something very complex, stick to VPL
That said, here’s some generated C# from our VPL…

## Slide 12: MSRS via C#
A quick look at and overview of some C# MSRS code and what VPL is doing under the hood

## Slide 13: What We Did
Overview of C# code
Pros
  Full MSRS functionality
Cons
  Extremely complex

## Slide 14: Building a ‘Bot
Building a robot controlled by an Xbox 360 controller, and a look at the C# under the hood

## Slide 15: Simulation Environment
Allows you to build a robot and environment without having the robot or environment
Full physics simulation via hardware or software

## Slide 16: Simulation Environment
A brief overview of what the simulation environment is and how it works

## Slide 17: Conclusion
MSRS is a very complex and feature rich environment for developing robotics software
Existing platforms allow one to easily get up and running
Generic/abstract services allow platform independence
CCR/DSS implement a lot of the grunt work required for concurrent and distributed programming
VPL provides for an easy-to-use rapid prototyping environment or simple robot design
Lego NXT is a very capable platform for building simple to moderately complex robots

## Slide 18: More Information
http://msdn.microsoft.com/robotics/
http://msdn.microsoft.com/coding4fun/robotics/
http://www.brianpeek.com/
brian@brianpeek.com

## Slide 19: Questions?