## Slide 1: Interfacing External Hardware Using .NET Managed Code
Brian Peek
Microsoft MVP – C#
brian@brianpeek.com
http://www.brianpeek.com/
http://www.aspsoft.com/
Level: Intermediate

## Slide 2: Agenda
Phidget Interface Kits
  I/O, both digital and analog
Servo controller
  Serial-based device
Nintendo Wii Remote (Wiimote)
  Connect to and use the Wiimote from .NET
If there’s time/interest
  Phidget RFID reader and tags

## Slide 3: Phidget Interface Kit 0/0/4
  Output board with 4 mechanical relays
    Relays capable of handling 250VAC , 10A (100VDC, 5A)
    Used to switch high-current devices
    I used this for my Christmas Lights project to switch strings of lights to music

## Slide 5: Phidget Interface Kit 0/16/16
  0/16/16 – 16 digital outputs, 16 digital inputs
    Used for digital I/O only (switches, LEDs, driving external devices)
    Inputs of 4V to 30V read as high
    Inputs of 0V to 3V read as low
    Provide external power for outputs, can sink up to 30VDC at 2 A.
    I used this with my R/C car project to toggle the switches used in the handset

## Slide 6: Phidget Interface Kit 8/8/8
  8/8/8 – 8 analog inputs, 8 digital inputs, 8 digital outputs
    Same as 0/16/16 with the addition of reading analog sensors (temperature, magnetic, sonar, accelerometer)
    Digital inputs are switch triggered, should not apply voltage
    Digital outputs are +5V when on and 0V when off
    Analog inputs receive voltage between 0 and +5V
      Converted into a value between 0 and 1000
      Phidget docs provide conversions to real units

## Slide 7: Phidget Interface Kit Examples
Simple example of analog and digital inputs and digital outputs

## Slide 8: Servos
Positional vs. Continuous Rotation
Pulse Width Modulation (PWM)
  Servos expect 50Hz PWM signal
    50 times/second, or 1 signal every 20ms
  Each pulse lasts from 0.5 to 2.5ms in length (width)
  1.5ms length pulses equate to centered/stopped
  0.5ms is 180° in one direction/full speed in one direction
  2.5ms is 180° in the other/full speed in the other

## Slide 9: PWM Diagram

## Slide 10: Lynxmotion SSC-32 Servo Controller
32 channels of 1uS resolution
Bidirectional communication (read and write)
Controlled via serial port and standard text commands
  #<ch> P<pulse width> S<speed> … #<ch> etc. <cr>
  Ex: #5 P1600 S750 <cr>
    Move servo 5 to position 1600 at 750uS per second until it reaches destination
Plenty of additional commands to handle offsets for calibration, querying of servo states, hexapod sequences, etc.
Used in our Finalizer battlebot

## Slide 12: Lynxmotion SSC-32 Servo Controller Example
Code to drive servos using SSC-32 via .NET SerialPort class

## Slide 13: Nintendo Wiimote (Wii Remote)
  3-axis accelerometer
    Can sense acceleration in 3 dimensions
  IR “camera”
    Can sense up to 4 IR points at 100Hz
    When used with a Wii, Sensor Bar provides 2 IR sources
  7 digital buttons + 4 direction D-pad
  4 LEDs
  Speaker
  Rumble/vibration feedback
  16KB EEPROM
  Bluetooth
  All at a cost of $40!

## Slide 14: Wiimote Extensions
Nunchuk
  3-axis accelerometer
  Analog joystick
  2 digital buttons
  Cost: $20
Classic Controller
  2 analog joysticks
  9 digital buttons
  2 analog buttons
  4 direction D-pad
  Cost: $20

## Slide 15: Wiimote Extensions
Guitar Hero III Controller
  Analog joystick
  5 fret buttons
  Whammy bar
  Strum bar
  2 digital buttons
  $60 for guitar only

## Slide 16: Wiimote Extensions
Wii Fit Balance Board
  Basically, a very expensive scale
  4 weight sensors at 4 corners
  At the moment, only included with Wii Fit which costs $90 (and is hard to find!)

## Slide 17: Connecting Wiimote to PC
Process is similar to any Bluetooth device
  Hold buttons 1 and 2 on Wiimote controller
  Scan for devices on PC
  Select “Nintendo RVL-CNT-01”
  Do not enter a security code/PIN
Once connected, 4 LEDs will continue to flash
Bluetooth is finicky and the Wiimote isn’t 100% Bluetooth compatible. Not all Bluetooth adapters or stacks will successfully pair with the Wiimote.

## Slide 18: Bluetooth/USB HID
Wiimote is detected as a Human Interface Device (HID)
HID devices can be communicated with in a very generic way
Allows devices to be “self-describing” by describing reports which can be sent to or received from the device
Keyboards, mice and other standard devices have pre-defined HID formats
The Wiimote only reports HID report lengths, not format so some reverse engineering is required

## Slide 19: HID From .NET
No support for HID in .NET
Must use P/Invoke to Win32 API
Full documentation available in Windows Device Driver Kit (DDK)
Process for connecting to Wiimote
  Get GUID of HID class
  Get handle to all devices in HID class
  With that handle, enumerate through all devices and get individual device handle
  With device handle, get device path
  Open device path using CreateFile Win32 function and retrieve vendor ID and product ID of device (VID = 0x057e, PID = 0x0306)
  If it matches, start read/writing the device
Device handle can be wrapped with FileStream object

## Slide 20: Wiimote From .NET
With that file handle, open asynchronous reading/writing
Reading
  Wiimote sends almost constant stream of HID reports with state information
    Reports are just a stream of bytes
    Data formats have mostly been reverse engineered, so it’s just a matter of parsing the byte stream into something useful
Writing
  Send HID report to Wiimote to tell it to “do something” such as turn on rumble, light an LED, etc.

## Slide 21: WiimoteLib
I’ve done the painful part and turned all of that into what is (I hope!) an easy to use library:
  Pair your Wiimote
  Call Connect() method
  SetReportType() method to tell Wiimote what data you want returned (buttons, accelerometers, extension controller, IR, etc.)
  Hook WiimoteChanged event which sends current state of Wiimote every time a report is received

## Slide 22: WiimoteLib Example
Overview of WiimoteLib code
Use the Wiimote and a Phidget Interface Kit to control an R/C car

## Slide 23: RFID
Radio-frequence Identification
Various standards which vary based on frequency and data length
Passive vs. Active
  Passive can be read from 0.5” to ~4” away without special hardware (even then, only 6”-12”)
  Active can be read up to 300 feet but require power source
Works via induction
  RF signal sent by reader induces electrical current in antenna located in RFID device
  Small current is enough power to transmit a response from the embedded CMOS IC

## Slide 24: RFID & Phidgets
Phidget board specifics:
  EM4102 standard
    125KHz
    Read-only
  40-bit unique identifier returned as hex string
    1,099,511,627,776 unique values
  4 outputs:
    5V for toggling relay on/off
    External LED
    Internal LED
    Antenna on/off
All controlled via eventing interface in .NET

## Slide 25: Phidget RFID Example
C# code to read value from RFID tag

## Slide 26: Summary
Phidget Interface Kits provide USB-based I/O with a simple API
Lynxmotion SSC-32 Servo Controller provides a very powerful interface to drive motors and servos via the serial port
  Note that Phidget now has several servo/motor controllers which are not as advanced, but are USB-based
USB/Bluetooth HID allows one to talk to any HID device, but must be done via native calls
The Nintendo Wiimote can provide a very unique interface to any application at a very cheap price

## Slide 27: More Information
Phidgets
  http://www.phidgets.com/
  http://www.trossenrobotics.com/
Lynxmotion SSC-32 Servo Controller
  http://www.lynxmotion.com/
Nintendo Wiimote
  http://www.codeplex.com/WiimoteLib
Other Projects Using These Items
  http://blogs.msdn.com/coding4fun/
  http://www.c4fbook.com/
    Due out November 2008
Me
  http://www.brianpeek.com/
  brian@brianpeek.com

## Slide 28: Questions?