## Slide 1: Get Connected with Kinect
Brian Peek
Senior Technical Evangelist
Microsoft
http://www.brianpeek.com/
brpeek@microsoft.com
Twitter: @BrianPeek
Level: Introductory

## Slide 2: Channel 9 / Coding4Fun
http://channel9.msdn.com/
http://www.coding4fun.com/

## Slide 3: Agenda
Kinect for Windows Hardware Overview
Kinect for Windows SDK Overview
  Color Camera
  Depth Camera
  Skeletal Tracking
  Audio
Extra tools to make life easier

## Slide 4: Kinect for Windows Hardware
IR Emitter
Color Sensor
IR Depth Sensor
Tilt Motor
Microphone Array

## Slide 5: Kinect USB Cable
A Kinect for Xbox 360 sensor can be used for development purposes with the USB power adapter
  Included with the standalone sensor
  Not included with an Xbox 360 system bundle

## Slide 6: Kinect for Windows SDK
Everything you need is at http://www.kinectforwindows.org/
  Download the SDK
  Order the Kinect for Windows Hardware
The Kinect for Xbox 360 hardware can be used for development, but redistributing a commercial application requires the Kinect for Windows hardware
  If the end-user has the runtime installed without the developer tools, the application will not run with a Kinect for Xbox 360 sensor

## Slide 7: Specs
Viewing angle | 43° vertical by 57° horizontal field of view
Mechanized tilt range (vertical) | ±27°
Frame rate (depth and color stream) | 30 frames per second (FPS)
Default resolution, depth stream | VGA (640 x 480)
Default tesolution, color stream | VGA (640 × 480)
Audio format | 16-kHz, 16-bit mono pulse code modulation (PCM)
Audio input characteristics | A four-microphone array with 24-bit analog-to-digital converter (ADC) and Kinect-resident signal processing such as acoustic echo cancellation and noise suppression

## Slide 8: System Requirements
Supported Operating Systems and Architectures
  Windows 7
  Windows Embedded Standard 7
Hardware Requirements
  32 bit (x86) or 64 bit (x64) processor
  Dual-core, 2.66-GHz or faster processor
  Dedicated USB 2.0 bus
  2 GB of RAM
  Graphics card that supports DirectX 9.0c
  A Kinect sensor!

## Slide 9: Sample Browser
Check out the Kinect Explorer sample

## Slide 10: Initialization
Get the KinectSensor object
Enable the streams you wish to read from
Hook the events for those streams
Start the KinectSensor

## Slide 11: Color Camera
Resolutions
Event passes a ColorImageFrame object
  Call the OpenColorImageFrame method to get the ColorImageFrame data object
  Call CopyPixelDataTo to get the image data itself as a byte array
  Use the “using” pattern…
Color Type | Resolution | FPS
RGB | 640x480 | 30
RGB | 1280x960 | 12
YUV | 640x480 | 15
YUV | 640x480 | 15

## Slide 12: Color Camera Example
Get data from the color camera

## Slide 13: Depth Camera
Returns the distance in millimeters and player for every pixel
Resolutions
Events pass a DepthImageFrame object
  Call the OpenDepthImageFrame method to get the DepthImageFrame data object
  Call CopyPixelDataTo to get the depth data itself as a byte array
  Use the “using” pattern…
Resolution | FPS
640x480 | 30
320x240 | 30
80x60 | 30

## Slide 14: Depth Data Calculations
Each Depth position is a 16-bit short value packed with both the distance and player index (if a player is recognized)
Distance
  int depth = depthPoint >> DepthImageFrame.PlayerIndexBitmaskWidth;
Player
  int player = depthPoint & DepthImageFrame.PlayerIndexBitmask;
Data Layout per 16-bit short
  D = Depth Data
  P = Player Index
D | D | D | D | D | D | D | D | D | D | D | D | D | P | P | P
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 15: Distances
Mode | Depth & Player | Center Hip Joint | Other 19 Joints
Default | Yes | Yes | Yes
Near | Yes | Yes | No, for v1.0

## Slide 16: Depth Camera Example
Getting data from the depth camera

## Slide 17: Skeletal Tracking

## Slide 18: Skeleton Data
Events pass a SkeletonFrame object
  Call the OpenSkeletonFrame method to get the SkeletonFrame data object
  Call CopySkeletonDataTo to get the skeleton data itself as an array of Skeletons
  Use the “using” pattern…
Skeletons contain an array of Joints
  Each Joint has an X,Y,Z position in 3D space

## Slide 19: Tracking States
Skeleton Tracking
Joint Tracking
State | Description
NotTracked | Not tracked
PositionOnly | Only skeleton position, no joints
Tracked | Skeleton position and joints
State | Description
Inferred | “Guesstimate”
NotTracked | Not tracked
Tracked | Accurate tracking

## Slide 20: Selective Skeleton Tracking
Two players can be tracked at once
Each skeleton has a unique identifier named TrackingId
On the SkeletonStream…
  Set AppChoosesSkeletons to true
  Use ChooseSkeletons method to choose which skeletons to track

## Slide 21: Skeleton Tracking Example
Getting skeleton data

## Slide 22: All Frames
You can hook up the AllFramesReady event to be notified, in sync, when all Enabled frames are ready
The event arguments allow you to open the appropriate frames and interact with the data as was just demonstrated

## Slide 23: AllFramesReady Example
Getting all frame data at once

## Slide 24: Audio
Kinect contains an array of 4 microphones
Because of this, the Kinect can return audio data AND audio source position
AudioSource is a Stream representing the incoming sound data
  Use this to record or interact with the sound data directly
  Data is in 16kHz, 16-bit mono PCM format
SoundSourceAngle and SoundSourceAngleConfidence determines where the sound is coming from

## Slide 25: Audio Example
Base audio example

## Slide 26: Speech Recognition
Integrates with the Microsoft.Speech library
On the KinectAudioSource:
  Set the EchoCancellationMode to None
  Set AutomaticGainControlEnabled to false
Get the Kinect Recognizer
Pass it to the SpeechRecognitionEngine
Setup a Grammar (words/phrases the speech engine will identify)
Hook up the SpeechRecognized, SpeechHypothesized, and SpeechRecognitionRejected events
Ensure AutomaticGainControlEnabled is set to false!

## Slide 27: Speech Recognition Example
Recognize speech with the Kinect microphone array

## Slide 28: Coding4Fun Kinect Toolkit
Easily convert Kinect data types to images
Scale joint data to larger display area
HoverButton control
http://c4fkinect.codeplex.com/
  Also available as a NuGet package

## Slide 29: Coding4Fun Kinect Service
Send Kinect data to another computer or even a Windows Phone
http://kinectservice.codeplex.com/
  Also available as a NuGet package

## Slide 30: Kinect Service Example
Sending Kinect data to a Windows Phone

## Slide 31: Included WPF Viewers
Located at:
  C:\Program Files\Microsoft SDKs\Kinect\v1.0\Samples\C#\KinectWpfViewers
Contains user control visualizers for all of the Kinect frame types
Also contains logic to determine if the right (or any) sensor is connected
These are a great way to get the data into your application with minimal effort

## Slide 32: Summary
Kinect is awesome
The Kinect for Windows SDK is pretty easy and straightforward to use
Use the C4F Kinect Toolkit to make your life even easier
Use the C4F Kinect Service to use Kinect as a remote service
Start building!

## Slide 33: Resources
Me
  brpeek@microsoft.com
  http://www.brianpeek.com/
  http://channel9.msdn.com/coding4fun/
Kinect for Windows SDK and Documentation
  http://www.kinectforwindows.org/
Kinect for Windows Blog
  http://blogs.msdn.com/b/kinectforwindows/
Coding4Fun Kinect Toolkit
  http://c4fkinect.codeplex.com/
  NuGet Package available directly
Coding4Fun Kinect Service
  http://kinectservice.codeplex.com/
  NuGet Package available directly
Coding4Fun Kinect Blog
  http://channel9.msdn.com/coding4fun/kinect